## Slide 1
Wave capturing process
Logic
Parts and Limitations
Flow
To discuss:

## Slide 2
Wave Capturing Process
Waveform Capture
Original Waveform (with sagging)
Trigger Time
PQ Capture
Trigger Time
What can waveform capture can look like:
What can PQ Capture can look like:

## Slide 3
Wave Capturing Process
Waveform Capture
Capture Duration (s)
Duration (W) = Total Cycles *
Duration (W) = 32 Cycles *
Duration (W) = 533 ms
PQ Capture
Total Event duration (s)
Duration (W) = Total Cycles * Period
Not to scale
Duration (PQ) = Duration of Input

## Slide 4
Logic
Waveform Capture
Trigger Time
PQ Capture
Trigger Time (W) = Start Time (PQ)
Duration (W) = Total Cycles *
Wave Duration (PQ) = Set duration of event in power source
Trigger Value = Threshold ± Boundary
Start Time = Trigger Time
For both logs to be Valid, the following must be satisfied:
(Default Total Cycles value varies depending on the meter)
(Threshold can be a user defined value or based on specifications)
# Wave Logs = # Sag/Surge Events set in the source

## Slide 5
Parts & Limitations:

## Slide 6
Display only for now
Assuming all events have the same duration
Assuming all meters have the same class.
Parts & Limitations:

## Slide 7
This only reflects the Sequence of events programmed in the Omicron’s State Sequencer Tool
Manually input only.
Only Channel and % Value Column are editable.
The checker can only process sequence of events like this. One events at a time.
Parts & Limitations:
Editable Cells

## Slide 8
Editable Cells
Satisfactory or With Issue
Will only be filled if there is an issue. There is a count for each.
Parts & Limitations:

## Slide 9
Flow:
Configuration Tab must be filled with info.
3 Phase System Tab should be filled with the script.
The user will select a meter type and will import logs.
The user must import Waveform logs first before the PQ logs. (another step are still unhandled)
The logs will then be pasted and will be organized in a newly created sheet named after the meter name.
Lastly, the user will click process to analyze the data and will be able to see the evaluation table and red markings if there is an issue.

## Slide 10
Flow:
The user will select a meter type and will import logs.

## Slide 11
Flow:
The user must import Waveform logs first before the PQ logs. (another step are still unhandled)

## Slide 12
Flow:
The logs will then be pasted and will be organized in a newly created sheet named after the meter name.

## Slide 13
Flow:
Lastly, the user will click process to analyze the data and will be able to see the evaluation table and red markings if there is an issue.

## Slide 14
Flow:
Lastly, the user will click process to analyze the data and will be able to see the evaluation table and red markings if there is an issue.